## Slide 1: From Shallow Learning to Deep Learning - Evolution of Machine Learning Algorithms for Ultrasonic NDT Applications
Erdal Oruklu,
Associate Professor
Electrical and Computer Engineering Department
Illinois Institute of Technology
Chicago, IL USA

## Slide 2
Motivation
Introduction to Ultrasonic Non-Destructive Testing (NDT) and Time-Frequency Analysis
Classical Machine Learning Methods for Ultrasonic Flaw Detection
Deep Learning Methods for Ultrasonic Flaw Localization and Classification
Conclusion
Agenda

## Slide 3
Development and advancement of technologies like IoT, Cloud Computing has paved way for more advanced manufacturing and industrial automation.
Automated inspection with minimal human intervention is the primary objective.
Similar paradigm shifts exist for NDE/NDT and Industrial automation applications (NDE 4.0) [*]
[*] Meyendorf, N., “Re-inventing NDE as science- How Student Ideas will help adapt NDE to New Ecosystem of science and technology,”AIP Conference Proceedings 1949,pp.1-10,April 2018[Online]. Available: https://aip.scitation.org/doi/abs/10.1063/1.5031518.
Motivation
Industrial Revolution 1.0
Industrial Revolution 2.0
Industrial Revolution 3.0
Industrial Revolution 4.0
NDT/NDE
1.0
NDT/NDE
2.0
NDT/NDE
3.0
NDT/NDE
4.0
Mechanization
Waterpower
Steam Power
Mass production
Assembly line
Electricity
Computation
Automation
Cyber Physical Systems
Human senses
(Visual and Sound)
Manual Inspection
Liquid Penetration Testing
Magnetic Particle Testing
Ultrasound testing
Eddy current testing
Radiography testing
IoT, Big Data,
Sensor Network,
Automated Monitoring

## Slide 4: Ultrasonic NDT and Setup
There are different types of Ultrasonic NDE/NDT test rigs for structural inspection.
The signals that are of interest are A-scan (Amplitude Scan) and B-scan (Brightness Scan).
Experimental A-scan data are acquired from broadband Ultrasonic sensor (Panametric A-3062) 0.375 in diameter with 5MHz central frequency and 100 MHz sampling rate.
Simulated data generated by OnScale and k-Wave are also used.
Courtesy of ECASP Research Laboratory: ecasp.ece.iit.edu

## Slide 5: Ultrasonic Flaw Detection
In ultrasonic imaging systems, the patterns of detected echoes, often complex and non-stationary, correspond to the location, shape, size, and orientation of the reflectors and the scattering properties of the propagation path.
Several signal modeling and estimation methods exist for ultrasonic echo classification, detection, recognition, and compression objectives.
This talk will cover:
  Time Frequency Analysis
  Machine Learning
    Supervised and Unsupervised
  Deep Learning
What are the advanced NDT applications made possible by ML?
What are the implications for computational requirements?

## Slide 6: Time-Frequency Analysis of Ultrasonic Signals
Wavelet Decomposition
Subband decomposition- observation channels
Filter locations
Transducer Bandwidth
Flaw detection using T/F analysis (subband filters)
Dynamically Reconfigurable Architecture Design for Ultrasonic Imaging”, by E. Oruklu et al., IEEE Transactions on Instrumentation and Measurement, vol. 58, no. 8, pp. 2856-2866, August 2009.

## Slide 7: T/F Analysis and Post-Processing Detectors
Target detection can be improved through multiple observations and post-detection processing.
  Order Statistics
  Neural Networks

## Slide 8: Detection Performance
“Dynamically Reconfigurable Architecture Design for Ultrasonic Imaging”, by E. Oruklu et al., IEEE Transactions on Instrumentation and Measurement, vol. 58, no. 8, pp. 2856-2866, August 2009.
“Hardware Efficient Realization of a Real-Time Ultrasonic Target Detection System”, by E. Oruklu et al., IEEE Transactions on Ultrasonics, Ferroelectrics and Frequency Control, vol. 56, no. 6, pp. 1262-1269, June 2009.
NN detector offers the most robust performance.

## Slide 9: Introduction to Machine Learning
Machine Learning is a technique to teach a self adaptive algorithm with real data, the algorithm “learns” while training. General design of any machine learning algorithm involves three steps:
  Design of Inference function involves finding a function which can produce the kind of output needed to solve a given problem.
  Design of cost function involves using a metric to wrap the inference function based on which optimization performance can be evaluated during training.
  Solution to cost function step involves optimizing the cost function using numerical analysis
Two main classes of Machine Learning (ML) include:
  Supervised Machine Learning
  Unsupervised Machine Learning
Depending on number of analytical stacks present, ML methods can be classified as:
  Classical (Shallow) Machine Learning (Logistic Regression (LoR), Support Vector Machine(SVM), Neural Networks (NN), Hidden Markov Models (HMM).
  Deep Learning (Convolutional Neural Networks, Deep Belief Network, RNN)

## Slide 10: Shallow (Supervised) Machine Learning
Supervised learning
Common steps for
  Logistic Regression (LoR)
  Neural Networks (NN)
  Support Vector Machines (SVM)
  Hidden Markov Model (HMM)

## Slide 11: Feature Selection for ML networks
Discrete Wavelet Transform is used as a preprocessing step:
  Time/Frequency analysis - leads to noise reduction.
  Reduced computation (subsampling in time).
According to energy distribution analysis of subbands, Low-pass, Low-pass (LL) component is selected as the input feature.
Either the entire DWT could be used as input or the signal could be windowed and provided as input.
Windowing (segmentation) approach was chosen.

## Slide 12
Logistic Regression (LoR) is general terminology for inference functions producing probabilistic output.
  Three optimization algorithms were tried: Steepest Gradient Descent Method(SGD), (Broyden–Fletcher–Goldfarb–Shanno) BFGS Method and conjugate gradient descent method (CGD).
Neural Networks (NN) provides flexibility in the architecture and easy discernment of data in non-linear cases.
  Each Neuron in a layer is nothing more than a logistic regression in terms of functionality.
  Many different ways to formulate the inference function.
Support Vector Machine, unlike LoR or NN, is constrained to two values as SVM is a binary classifier.
  Kernels chosen to transform functions for linear separation
Supervised ML algorithms
K. Virupakshappa and E. Oruklu, "Investigation of Feature Inputs for Binary Classification of Ultrasonic NDT Signals using SVM and Neural Networks," 2019 IEEE 62nd International Midwest Symposium on Circuits and Systems (MWSCAS), 2019, pp. 638-641, doi: 10.1109/MWSCAS.2019.8884852.

## Slide 13: Hidden Markov Models
It is state-based statistical supervised ML algorithm.
Discrete states with discrete probability distribution function is chosen for this implementation.
Learning algorithm finds the transition and emission probability matrices. The maximum likelihood estimates of the parameters of HMM needs to be found using Baum-Welch Algorithm.
K. Virupakshappa and E. Oruklu, "A hardware/software co-design architecture for ultrasonic flaw detection with Hidden Markov Model and wavelet transform," 2017 IEEE International Ultrasonics Symposium (IUS), 2017, pp. 1-1, doi: 10.1109/ULTSYM.2017.8092037

## Slide 14: Unsupervised Machine Learning
K-means classification is based on clustering
  The cost function is to minimize the distance metric
Gaussian Mixture Modeling (GMM)
  statistics based unsupervised learning algorithm
Detection accuracy of above 90% was observed for both K-means clustering and GMM. But the flaw detection is delayed (shifted) by a fixed amount.
K. Virupakshappa and E. Oruklu, "Unsupervised Machine Learning for Ultrasonic Flaw Detection using Gaussian Mixture Modeling, K-Means Clustering and Mean Shift Clustering," 2019 IEEE International Ultrasonics Symposium (IUS), 2019, pp. 647-649, doi: 10.1109/ULTSYM.2019.8926078.

## Slide 15: Comparison for Shallow Machine Learning
NN is the most robust performer with more computational requirements
FPGA implementation (Xilinx Zynq platform)

## Slide 16
DL is also known as hierarchical learning as layers are stacked to get additional features before performing the final prediction/classification
Several architectures:
  Convolutional Neural Networks (CNN)
  Deep Belief Networks (DBN)
  Recurrent Neural Networks (RNN)
CNN: Contains one or more convolutional layers. Unaffected by translation, rotation, dilation, thus useful in image processing
DBN: Unsupervised learning layers stacked on one another and finally any classifier can be used as final layer.
RNN: Involves feeding of past output back into NN with current inputs. Has memory, popular in text/speech recognition algorithms.
Deep Learning Algorithms
[*] Y.LeCun, L. Bottou, Y. Bengio, and P. Haﬀner, “Gradient-based learning applied to document recognition,” Proceedings of the IEEE, November 1998, pp. 1–46.
[**] https://www.ibm.com/cloud/learn/recurrent-neural-networks
[***] https://medium.com/black-feathers-labs/deep-belief-networks-an-introduction-1d52bb867a25
CNN [*]
DBN [**]
RNN [***]

## Slide 17: Deep Learning for Ultrasonic Analysis
Initial work: Flaw detection using two different CNN models
  A-scan data initially processed by the wavelet transform
  Robust performance
More challenging problems:
  Multi-class classification of flaw types
  Can we design a generalized deep learning pipeline for Ultrasonic flaw analysis?
Proposed solution:
  Flaw localization and classification using Meta Learning
  Localization is generally applied to select a specific region of-interest (flaws) and check if there is a flaw. This approach reduces loss of information while down-sampling the signal/images for classification or any further analysis.

## Slide 18: CNN Architectures for Flaw Detection
CNN is among the key Deep Learning algorithms that have gained increased attention in recent years due to their success in machine vision, pattern recognition and classification tasks.
  CNN consists of multiple layers, and it can extract features in a hierarchical manner to construct a high-level abstraction of the original data.
  Usually, a CNN consists of several layers of Convnets followed by a fully connected Neural Networks.
  Each Convnet has a convolution filter stage (multiple filters), followed by a pooling or activation layers.
We propose two CNN architectures (based on 1D-CNN and LeNet models) for ultrasonic data (A-scan) using wavelet coefficients as feature inputs and investigate key topologies such as number of parallel convolution networks, number of filters and output classifier.

## Slide 19: Input Feature Selection for CNN
The wavelet feature selection has been done using the energy distribution analysis on the A-scan data (acquired from steel blocks containing flaws such as Flat Bottom Hole). Wavelet kernels used in the analysis include Coiflet-5, DB-10, Symlet-6 and Symlet-8.
The wavelet decomposition is done at several levels and the results are tabulated in Tables 1-4.

## Slide 20: Algorithm 1: Ultra-1D CNN
Ultra- 1D CNN has 4 pipelines of 1D Convnets with each pipeline receiving one the components of DWT output at fourth level of decomposition.
Each pipeline has 3 1d convnets containing convolution layer followed by maxpool layer. Activation function used for convnet was ReLu.
1st layer has 1x5 Convolution with with a stride of 1 and depth 5. Output after maxpooling is of length 62.
K. Virupakshappa, M. Marino and E. Oruklu, "A Multi-Resolution Convolutional Neural Network Architecture for Ultrasonic Flaw Detection," 2018 IEEE International Ultrasonics Symposium (IUS), 2018, pp. 1-4, doi: 10.1109/ULTSYM.2018.8579888.

## Slide 21: Algorithm 2: Ultra-LeNet
The second architecture investigated is a LeNet [*] inspired architecture.
Here the input is the DWT components but treated as a 2D data.
1st layer has 2x10 convolution with a depth of 6 followed by 2x2 maxpooling. Again, the activation layer used is ReLu.
[*] Y.LeCun, L. Bottou, Y. Bengio, and P. Haﬀner, “Gradient-based learning applied to document recognition,” Proceedings of the IEEE, November 1998, pp. 1–46.
K. Virupakshappa, M. Marino and E. Oruklu, "A Multi-Resolution Convolutional Neural Network Architecture for Ultrasonic Flaw Detection," 2018 IEEE International Ultrasonics Symposium (IUS), 2018, pp. 1-4, doi: 10.1109/ULTSYM.2018.8579888.

## Slide 22: Results for CNN based Flaw Detection
Proposed architectures were trained with DWT inputs of 800 A-scans.
Each architecture was run for 100 epochs to get validation accuracy.
Overall accuracy for simulation data was found to be 94% while accuracy on experimental data was found to be 92% for Ultra-LeNet.
Ultra-LeNet Performance
K. Virupakshappa, M. Marino and E. Oruklu, "A Multi-Resolution Convolutional Neural Network Architecture for Ultrasonic Flaw Detection," 2018 IEEE International Ultrasonics Symposium (IUS), 2018, pp. 1-4, doi: 10.1109/ULTSYM.2018.8579888.
Yuan, Y., Virupakshappa, K. & Oruklu, E. FPGA Implementation of an Ultrasonic Flaw Detection Algorithm Based on Convolutional Neural Networks. J Sign Process Syst (2022). https://doi.org/10.1007/s11265-022-01756-5

## Slide 23: Deep Learning for Ultrasonic Flaw Localization and Classification
Can we detect and classify multiple flaw types?
  Preliminary work
Localization of the Region of Interest (ROI) in B-scan data, which contain Ultrasound reflections and diffractions belonging to a specific flaw type, is an important step for automating the Flaw Classification or Characterization process.
  Accurate localization of Ultrasonic flaws in a raw B-scan can facilitate complex classification tasks such as Multi-class flaw detection or estimating the dimension and/or the orientation of the flaw.
  We propose a regression-based algorithm to find a bounding box which localizes the reflections and diffractions associated with the flaw in a planar raw B-scan.
  The proposed method is a grid-based localization algorithm which uses Deep Learning to find the Region of Interest as a bounding box. The bounding box should essentially contain all the reflections and diffractions belonging to a specific flaw class and should be able to generalize irrespective of the flaw type.
Next, a new DL classifier is introduced which uses meta-learning to generalize the inference operations and data training.

## Slide 24: Data Setup and Simulations
An immersion test setup with a specific type of void has been simulated for this work. The immersion liquid used is water and the metal block under inspection is steel. The transducer is a sensor array operating at central frequency of 5 MHz.
All data synthesis have been performed using OnScale simulation software.The voids (flaws) that are being classified are listed below:
  Side Drilled Hole (SDH).
  Flat Bottom Hole (FBH).
  Rectangular Void with length greater than width (RVLgW).
  Rectangular Void with width greater than length (RVWgL).
Example B-scan images corresponding to each flaw type are shown below.

## Slide 25: A New Generalized DL Pipeline
A new generalized pipeline based on a Grid Based Localizer and a Meta Learning based classifier is introduced.
Grid Based Localizer is regression based deep learning algorithm which extracts Region of Interests (flaws) in a B-scan.
Meta Learning is a “Learning to Learn” algorithm which uses meta data to make decisions like classification rather than use memorized features (as in CNN).
This pipeline is generalized because it is independent of number and type of flaws/voids in B-scan making it a new approach at solving localization and classification.
RVWGL: Rectangular void with Width greater than length
RVLGW: Rectangular void with Length greater than width

## Slide 26: Grid Based Localization
Grid Based Localization is Supervised Deep learning algorithm which extracts region of interest/interests from B-scans influenced by algorithms such as YOLO and RCNN. Unlike in YOLO or RCNN the new proposed method is a regression-based algorithm.
This design is compared against a Contour based localizer which uses morphological functions.
Input to the deep learning algorithm is the B-scan and desired output is the grid indicators for bounding box.
If the inputs are divided as grids, then the output of the deep learning algorithm should be a matrix (or a flattened vector) of corresponding grid size indicating the presence (Regions 0 and Regions 1) or absence of bounding box.
The matrix is flattened along the rows. This flattened vector is the output of Deep Learning algorithm.
K. Virupakshappa and E. Oruklu, "Localization of Ultrasonic Flaws using Grid Based Deep Learning," 2021 IEEE International Ultrasonics Symposium (IUS), 2021, pp. 1-3, doi: 10.1109/IUS52206.2021.9593753.

## Slide 27: Grid Based Localizer Network
The input B-scan is resized to 400 x 400 from the original resolution.
The output is the flattened version of the encoded grids and for this work each grid size was chosen to be 5 x 5, so the number of grids is 80 x 80. The flattened version of the output has 6400 neurons.
Each convolutional layer seen has convolution filter operation, batch normalization, ReLu activation followed by Max-pooling.
Convolution operation acts as feature selector. Batch Normalization is used to keep the output values of convolution in a range, along the batch axis to avoid co-variance shift. ReLu activation is used to help backward propagation error gradient reach the very end of the convolution layer, while Max-pooling is used to decrease the input size and extract features for the next layer, so that processing can be simple for the next convolution layer.
The fully connected neurons at the end has ReLu activation except for the final output which has Linear activation function.
Mean Square Error is used as the loss function for optimization, hence treating the whole algorithm as supervised linear regression problem

## Slide 28: Grid Based Localization
Examples: 60 B-Scan data containing 2 voids and 60 B-scan data containing a single void were used for testing.
  60 B-scans of training data were randomly selected from 1500 single void B-scans and 60 B-scans of training data were randomly selected from 1500 double void B-scans. This data were used to determine the threshold for the grids.
RVWGL: Rectangular void with Width greater than length
RVLGW: Rectangular void with Length greater than width
FBH: Flat Bottom Hole
SDH: Side Drilled Hole

## Slide 29: A New Classifier Design-Introduction to Meta Learning
Meta Learning involves use of meta-data belonging to each task/class that needs to be recognized. Meta Learning have evolved over several decades from being metric based algorithms such as Nearest Neighbor based approach to adaptation of Convolutional layers and neural networks.
Meta Learning algorithms use templates/reference data belonging to a specific task/class which is then used to compare with a query data. Images or signals can be directly used, or features can be extracted from the images or signals and then used with meta learning algorithm.
  A criteria or function that measures similarity between the data or features can be used as a metric to decide the similarity between the template. If the value of the function favors the similarity criteria, then the query data belongs to the task/class of the template.
  The features extracted from the data are generalized/automated such that the feature extraction algorithm (encoder algorithm) can be used on any new tasks or classes. In Convolutional network-based feature extractors, this is known as Encoder networks.

## Slide 30: Meta Learning Classifier
The model can only tell, if the template and query data are similar or not but there can be additional concepts used to make inference and judgments.
The generalization capability of meta learning comes from the fact that training classes and testing class can be completely different i.e., for this work one of the instances of experimentation involves use of SDH, RVLGW and RVWGL for training, while FBH with the training classes have been used for inference.
  Although FBH was not used for training the inference algorithm still works on FBH without making any change to the algorithm.
K. Virupakshappa and E. Oruklu, "Automatic Feature Extraction Based on Meta-Learning for Ultrasonic Flaw Classification," 2020 IEEE International Ultrasonics Symposium (IUS), 2020, pp. 1-3, doi: 10.1109/IUS46767.2020.9251444.

## Slide 31: Siamese Network Based Meta Learning
Siamese network architecture used in this work has an encoder and a classifier.
The encoder consists of convolutional layers and the classifier is a comparison metric or a neural network.
  Each convolutional layer consists of Convolution filtering, batch normalization, ReLu activation followed by Max-pooling in the encoder network.
The classifier consists of l1 norm-based classifier which uses sigmoid function on the l1 norm of the template and query features obtained from the encoder output.
  If there is similarity between the template and query features, then the score is 1 else the score is 0, so a sigmoid activation function is used at output.

## Slide 32: Other DL Classifiers Tested for Multi-Class Detection
In order to compare the difference in performance with existing algorithms, CNN and DBN architectures have been used as references.
One hot encoded CNN is used as a baseline comparison.
DBN is a semi-supervised learning algorithm, and it is one of the earliest versions of generative networks employed for both encoding decoding purposes.
  Restricted Boltzmann Machine (RBM) layers, which extract the features, are unsupervised learning layers in the Deep Belief Network. The features extracted from the RBM’s are used for classification using supervised classifiers like Neural Network or Support Vector Machine or Logistic Regression.
K. Virupakshappa and E. Oruklu, "Multi-Class Classification of Defect Types in Ultrasonic NDT Signals with Convolutional Neural Networks," 2019 IEEE International Ultrasonics Symposium (IUS), 2019, pp. 1647-1650, doi: 10.1109/ULTSYM.2019.8926027.

## Slide 33: Results - Localizer Performance
In this comparative experiment, the normalized area (NA) has been used to compare the Ground Truth (GT), Contour Based Localization (CBL) and Grid Based Localization (GBL) for a single void in B-scan. NA is defined as:
where W= Width, H=Height, ROI=Region of Interest.
Results show that GBL outperforms CBL(morphological operations) and achieves similar (slightly higher) normalized area on average when compared against Ground Truth.

## Slide 34: Results – DL Classifier Performance
The localized data was subjected to classification and for different algorithms the accuracy obtained for different algorithms are as shown in the Tables below.
  The percentage represents the true positive cases where the specific test B-scan is inferred to belong to the actual class.
For Meta Learning FBH class was not used during training; thus proving generalization.
CNN has very high accuracy but cannot generalize without training while Siamese net has good accuracy but can generalize. DBN is unable to match CNN or Siamese net classifier performance.

## Slide 35: More Observations on Meta Learning
The effect of clutter on Meta Learning and CNN shows the robustness of Meta Learning. With increase in clutter, accuracy drops faster for CNN. Generalization with Siamese net is still achievable with the addition of clutter.
The second table shows the 5-way accuracy of the FBH and SDH-SDH classes. SDH-SDH class refers to the case where two SDH holes are present in the steel block.
Though accuracy of the Meta-Learning seems to be constant, within class confidence decreases with increase in clutter and within class confidence on untrained class FBH is low.

## Slide 36
ML learning algorithms demonstrate very robust performance for ultrasonic flaw detection even in presence of significant clutter noise.
  There are computationally efficient algorithms which are suitable for embedded systems (i.e., edge computing) such as LoR and NN.
DL algorithms are evolving very rapidly and there are many architectures suitable for analyzing raw Ultrasonic signals (A-scan and B-scan data).
While DL is not necessary for binary classification tasks (detection), more challenging problems can be solved with specialized DL networks.
  These tasks can include multi-class detection (distinguish flaw types) or material characterization among others.
  Main challenge for DL is obtaining sufficient experimental training data and the computational issues.
We are currently investigating simulated/experimental data sets as well as compressed DL network models for real-time hardware implementation (inference only).
Conclusion

## Slide 37: Thank you!
QUESTIONS?
Contact:
  ERDAL ORUKLU
  oruklu@iit.edu